## Slide 1: AUE 817 Final Project Presentation
Team 3:
Darui Zhang, Bin Xu, Liang Li
Sizing and Controlling of a Parallel Hybrid SUV Powertrain
April 30 2014
Clemson University CU-ICAR

## Slide 2: Project Overview
Process Flow
Components Sizing
Fuel Economy
(MPG<34.6 MPG)
Power
(0-60 mph time<9s)
Components sizing need to consider the competing requirements of fuel economy and power. Bigger engine means higher power and lower efficiency.
Iteration is needed due to the change of one component will affect other components and total weight.
Updating Control Strategy
Iteration

## Slide 3: Vehicle Configuration
Project Overview
Engine
Torque
Converter
Gear box
Differential
Front wheels
Vehicle
Electric
motor
Battery
Gear
Differential
Rear wheels
Note: Engine and electric motor are connected by road
Vehicle parameters:
Frontal area A = 2.48 m^2
Curb weight = 1300 kg, GVWR = 1750 kg
Rolling resistance coefficient = 0.008
Aerodynamic drag coefficient Cd = 0.32
Tire size: 255/55R18, dynamic rolling radius = 357mm
Rotating inertia: 1.4 kgm2 (per wheel)
Transmission:
4 speed Automatic Transmission:
Gear ratio: 2.847, 1.552, 1.000, 0.700
Differential ration: 4.13
Shift points under normal driving loads
12 1,500 RPM
2 2,000 RPM
3 2,500 RPM

## Slide 4: Powertrain Sizing
Engine
_dot B S
……
Excel data
New engine
Linear extrapolation method

## Slide 5: Powertrain Sizing
Engine
Maximum torque:
174 Nm @4400 RPM
Maximum Power:
98 kW @6000 RPM

## Slide 6: Powertrain Sizing
Motor
1. Willan’s line model: Convert initials motor efficiency map from Torque and RPM to pme (mean effective pressure) and cm (mean piston speed).
2. Curve fitting (Least square method): parameterize e and ploss with polynomial functions of cm.
3. Sizing: Convert dimensionless model back to dimensional model to acquire the efficiency map of a machine of new size
2. Curve fitting
Dimensionless model
3.Dimensional model
1.Convert Initial map to pme and cn

## Slide 7
As is done in HW4, peukert effect is taken into consideration, and the least square fitting method is implemented when building up the battery model. Validation is executed, and the results show the fitting is acceptable.
Powertrain Sizing
Battery Pack
Peukert Equation Fitting
Picking points using Plot Digitizer
Validation for both discharge & charge

## Slide 8
Results
Powertrain Sizing
Battery Pack
R_vs_SOC_disch
V_oc_vs_SOC_disch
R_vs_SOC_ch
V_oc_vs_SOC_ch

## Slide 9
Powertrain Sizing
Battery Pack
Thermal Model Description
E=fcn(SOC, T, I)
Thermal Model added
Subsystem: Obtain SOC
Three inputs
Determine which map to use

## Slide 10
Powertrain Sizing
Battery&Fuel tank Pack
Fuel tank sizing
Volume: 8.5 gallon with 350 miles UDDS&HWFET combined cycle
Battery sizing
Volume: 144 Litrers
Mass: 105 kg
Cell: 247

## Slide 11: Control Strategy
ECMS
Equivalent Consumption Minimization Strategy (ECMS):
Minimize instantaneous fuel consumption instead of global
2. Discretization: Split torque between engine an motor
3. Calculation Equivalent fuel consumption of electrical motor
4. Minimize fuel consumption of Engine and Motor combined
1. Calculate motor speed at a given engine speed by gear ratio.
Steps:
;

## Slide 12: Control Strategy
A 3+1D look up ( engine speed, torque request, x_soc + gear) table of motor torque request is pre-computed to reduce online computational cost.
Lookup Table
Note: X_SOC is mapping of SOC between [-1, 1]
As x _soc decreases, less is requested from electrical motor due to the penalty function on low SOC

## Slide 13: Control Strategy
Simulink Implement
Breaking
Torque Split
Sport mode for
(acceleration test)
Motor torque request
Lookup table
Powering

## Slide 14: Results
Urban (UDDS) Cycle
SOC
MPG: 56.18

## Slide 15: Results
Highway (HWFET) Cycle
SOC
MPG: 53.61

## Slide 16: Results
Accelerating (0-60 MPH)
Time: 8.29s

## Slide 17: Summary
Specifications:
Testing Results:
Fuel economy test | 
Cycles | MPG
UDDS | 56.18
HWFET | 53.61
combined | 54.99
US06 | **25.34
Cycle4.87 miles | 49.53
Cycle10.6 miles | 42.85
Acceleration test | 
Top speed | 103 mph
0-60 MPH | 8.29 sec
0-20 | 2.32 sec
20-40 | 2.50 sec
30-50 | 2.94 sec
50-70 | 3.89 sec
1/4 mi time | 19 sec
1/4 mi exit spd | 92 mph
*Note:
Weight factor 1.8
Engine specs | 
Max power | 64.7 kW @ 6000 RPM
Max Torque | 114.9 Nm @4400 RPM
Displacement | 1.3 L
Motor specs | 
Max Hp | 143 kW
Max Torque | 400 Nm (0-357 rad/s)
Radius | 57.6 mm
Length | 392 mm
Battery pack | 
Single battery capacity | 1729 Ah
Max power | 187 Kw
Battery cell weight | *105 kg
Number of cells | 247
Vehicle weight | 
Curb wieght | 1720 kg
Battery | 105 kg
Driver | 75 kg
Total | 1900 kg
**Note: low mpg due to aggressive acceleration and deceleration in the cycle. Change exceeds the battery maximum capacity. Battery cannot recuperate all the energy in breaking.
Goal:
Top speed >100 mph
0-60 mph: <9 sec
Goal:
Combined mpg
> 34.6
Downsizing + EM Boosting

## Slide 18: Thank you!
Questions?